## Slide 1: CDA 3103
Recitation 11 – Performance

## Slide 2: Performance
Performance is the key to understanding underlying motivation for the hardware and its organization
Measure, report, and summarize performance to enable users to
  make intelligent choices
  see through the marketing hype

## Slide 3: Computer Performance: TIME
Response Time (elapsed time, latency):
  how long does it take for my job to run?
  how long does it take to execute (start to
  finish) my job?
  how long must I wait for the database query?
Throughput:
  how many jobs can the machine run at once?
  what is the average execution rate?
  how much work is getting done?
Individual user
concerns…
Systems manager
concerns…
Notes: If we upgrade a machine with a new processor what do we increase?
If we add a new machine to the lab what do we increase?

## Slide 4: Definition of Performance
For some program running on machine X: PerformanceX = 1 / Execution timeX
“X is n times faster than Y” means: PerformanceX / PerformanceY = n

## Slide 5: Clock Cycles
Instead of reporting execution time in seconds, we often use cycles.
In modern computers hardware events progress cycle by cycle: in other words, each event, e.g., multiplication, addition, etc., is a sequence of cycles
clock rate (frequency) = cycles per second (1 Hz. = 1 cycle/sec, 1 MHz. = 106 cycles/sec)
Example: A 200 Mhz clock has a cycle time of 5 nanoseconds

## Slide 6: How many cycles are required for a program?
Multiplication takes more time than addition
Floating point operations take longer than integer ones
Accessing memory takes more time than accessing registers
Important point: changing the cycle time often changes the number of cycles required for various instructions because it means changing the hardware design.

## Slide 7: Performance Equation
CPU execution time for a program
Instruction count average CPI Clock cycle time for a program
=



## Slide 8: CPI Example I
Suppose we have two implementations of the same instruction set architecture (ISA). For some program:
  machine A has a clock cycle time of 10 ns. and a CPI of 2.0
  machine B has a clock cycle time of 20 ns. and a CPI of 1.2
Which machine is faster for this program, and by how much?
If two machines have the same ISA, which of our quantities (e.g., clock rate, CPI, execution time, # of instructions, MIPS) will always be identical?

## Slide 9: Solution
CPU timeA = IC × CPI × cycle time = IC × 2.0 × 10ns = 20 ×IC ns
CPU timeB = IC × 1.2 × 20ns = 24 ×IC ns
So, A is 1.2 (=24/20) times faster than B

## Slide 10: CPI Example II
A compiler designer is trying to decide between two code sequences for a particular machine.
Based on the hardware implementation, there are three different classes of instructions: Class A, Class B, and Class C, and they require 1, 2 and 3 cycles (respectively).
The first code sequence has 5 instructions:
1 of A, 1 of B, and 3 of C
The second sequence has 5 instructions:
2 of A, 1 of B, and 2 of C.
Which sequence will be faster? How much? What is the CPI for each sequence?

## Slide 11: Solution
# of cycles1 = 1 x 1 + 1 x 2 + 3 x 3
= 12
# of cycles2 = 2 x 1 + 1 x 2 + 2 x 3
= 10
Sequence 2 is 1.2 times faster
CPI1 = 12 / 5 = 2.4
CPI2 = 10 / 5 = 2

## Slide 12: Benchmarks
Performance best determined by running a real application
  use programs typical of expected workload
  or, typical of expected class of applications
    e.g., compilers/editors, scientific applications, graphics, etc.

## Slide 13: Amdahl's Law
Execution Time After Improvement =
Execution Time Unaffected + ( Execution Time Affected / Rate of Improvement )
Improved part of code

## Slide 14: Amdahl's Law Example I
Suppose we enhance a machine making all floating-point instructions run five times faster. The execution time of some benchmark before the floating-point enhancement is 10 seconds.
  What will the speedup be if half of the 10 seconds is spent executing floating-point instructions?

## Slide 15: Solution
Suppose we enhance a machine making all floating-point instructions run five times faster. The execution time of some benchmark before the floating-point enhancement is 10 seconds.
  What will the speedup be if half of the 10 seconds is spent executing floating-point instructions?
Execution Time After Improvement =
Execution Time Unaffected + ( Execution Time Affected / Rate of Improvement )
  Execution Time After Improvement = 5 + 5 / 5 = 5 + 1 = 6 seconds

## Slide 16: Amdahl's Law Example II
Consider program P, which runs on a 1 GHz machine M in 10 seconds. An optimization is made to P, replacing all instances of multiplying a value by 4 (mult X,X,4) with two instructions that set x to x + x twice(add X,X;add X,X). Call this new optimized program P’.
The CPI of a multiply instruction is 4, and the CPI of an add is 1. After recompiling, the program now runs in 9 seconds on machine M. How many multiplies were replaced by the new compiler?

## Slide 17: Solution
How many multiplies were replaced by the new compiler?
Let Number of multiplies replaced in new compiler = X
Number of cycles executed in the old compiler = 4X
Number of cycles executed in new compiler = 2X
Total number of cycles difference 4X-2X = 2X
Total number of cycles difference between P and P’
= 10*109 – 9*109 = 109
2X = 109 => X = 5 * 108

## Slide 18: Amdahl's Law Example III
Assume that multiply instructions take 12 cycles and account for 15% of the instructions in a typical program, an the other 85% of the instructions require an average of 4 cycles for each instruction. What percentage of time does the CPU spend doing multiplication?

## Slide 19: Solution
CPU Time for multiply instructions
CPU Time = IC * CPI * Clock cycle time
= IC*0.15 * 12 * CC
= 1.8*IC*CC
CPU Time for all instructions
CPU Time = IC * CPI * Clock cycle time
= (IC*0.15*12 + IC*0.85*4)*CC
= 5.2*IC*CC
Percentage of time CPU spend doing multiplication
1.8*IC*CC/5.2*IC*CC = 34.6%

## Slide 20: Amdahl's Law Example III, revisit
Your hardware engineering team has indicated that it would be possible to reduce the number of cycles required for multiplication to 8, but this will require a 20% increase in the cycle time. Nothing else will be affected by the change. Should they proceed with the modification?

## Slide 21: Solution
CPU Time for original hardware
CPU Time = IC * CPI * Clock cycle time
= (IC*0.15*12 + IC*0.85*4)*CC
= 5.2*IC*CC
CPU Time for new hardware
CPU Time = IC * CPI * Clock cycle time
= (IC*0.15*8 + IC*0.85*4)*1.2CC
= 5.52*IC*CC
Comparing original and new hardware
Performancenew/Performanceorg = 5.2*IC*CC/5.52*IC*CC
= 0.942
Modification should not be made because it reduces performance

## Slide 22: Performance Evaluation Example
For a typical workload, the percentages of groups of instructions and their average CPI are given in the following table.
Instruction | Percentage (%) | CPI
Integer | 50 | 1
Branch | 5 | 2
Load/Store | 30 | 4
Floating-point | 15 | 10

## Slide 23: Performance Evaluation Example
a. Calculate the overall average CPI for the typical workload.
b. There are three possible ways to make performance improvement.
  First, an enhanced compiler can reduce the floating-point instructions to ½ of the original floating-point instructions with the cost of increasing the integer instructions by 15% of the original integer instructions.
  Second, a new pipeline technique can reduce the average CPI of the floating-point instruction from 10 to 4 with an increasing clock cycle time of 4%.
  Third, an improved caching technique reduces the CPI of Load/Store from 4 to 3.
  Calculate and compare the performance improvement of the three solutions.

## Slide 24: Solution
a. Average CPI = 50%*1 + 5%*2 + 30%*4 + 15%*10 = 3.3
b. Old scheme: CPU time = 3.3*IC*Cycle Time
  First: ((50%*115%)*1 + 5%*2 + 30%*4 + (15%/2)*10) *IC*Cycle Time = 2.625*IC*Cycle Time
  Second: (50%*IC*1 + 5%*IC*2 + 30%*IC*4 + 15%*IC*4)*1.04*Cycle Time = 2.496*IC*Cycle Time
  Third: (50%*IC*1 + %5*IC*2 + 30%*IC*3 + 15%*IC*10)*Cycle Time = 3*IC*Cycle Time

## Slide 25: Question 6
Suppose a computer runs at 1GHz. If a typical application has the following distribution of instructions.
What’s the average CPI?
Instructions | Percentage (%) | CPI
Floating point | 20% | 3
Load | 30% | 2
Branches | 15% | 4
Integer | 10% | 1
Store | 20% | 1
Other | 5% | 1.5

## Slide 26: Question 6
Average CPI
= 0.2*3 + 0.3*2 + 0.15*4 + 0.1*1 + 0.2*1 + 0.05*1.5
= 2.175

## Slide 27: Summary
Performance is specific to a particular program
  total execution time is a consistent summary of performance
For a given architecture performance increases come from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Pitfall: expecting improvement in one aspect of a machine’s performance to affect the total performance

## Slide 28: Questions?