## Slide 1: CDA 3103
Recitation 10 – Control Signals

## Slide 2: MIPS Single Cycle Datapath

## Slide 3: Control Signals – Register Destination
RegDst
  Deasserted: the register destination number for the write register comes the rt field (bits 20:16)
  Asserted: the register destination number for the write register comes the rd field (bits 15:11)

## Slide 4: Control Signals – Register Write
RegWrite
  Asserted: the register destination on the write register input is written with the value on the write data input

## Slide 5: Control Signals – ALU Source
ALUSrc
  Deasserted: The second ALU operand comes from the second register file output
  Asserted: The second ALU operand is the sign-extended lower 16 bits of the instruction

## Slide 6: Control Signals – Memory Read
MemRead
  Asserted: Data memory contents designated by the address input are put on the read data output.

## Slide 7: Control Signals – Memory Write
MemWrite
  Asserted: Data memory contents designated by the address input are replaced by the value on the write data input.

## Slide 8: Control Signals – Memory to Register
MemtoReg
  Deasserted: The value fed to the register write data input comes from the ALU
  Asserted: The value fed to the register write data input comes from the data memory.

## Slide 9: Control Signals – Branch
Branch on Equal
  Deasserted: PC = PC + 4
  Asserted: Check Zero output of the ALU
    When Zero is asserted use the branch target address. PC = PC + 4 + 4*Instruction[15-0]

## Slide 10: Control Signals – Jump
Jump
  Deasserted: PC is either PC + 4 or the branch target
  Asserted: PC = PC + 4[31-28] : Instruction[25-0] * 4

## Slide 11: Setting Control Signals
Consider the single cycle datapath. What would be the values of the control signals for the following instructions: add, addi, lw, beq, j?