## Slide 1: CDA 3103
Recitation 8 – MIPS Practice Problems

## Slide 2: Question 1: R-Type and I-Type arithmetic
Convert the following C code into MIPS assembly. Assume that the values of f and g are assigned to $s0 and $s1 respectively.
f = g + (-f – 5);

## Slide 3: Question 1: R-Type and I-Type arithmetic
Convert the following C code into MIPS assembly. Assume that the values of f and g are assigned to $s0 and $s1 respectively.
f = g + (-f – 5);
Solution:
sub f, $0, f
addi f, f, −5
add f, f, g

## Slide 4: Question 2: Loading from Memory
Convert the following C code into MIPS assembly. Assume that the value of f is assigned to $s0 and the base address of A is stored in $s6.
f = f + A[2];

## Slide 5: Question 2: Loading from Memory
Convert the following C code into MIPS assembly. Assume that the value of f is assigned to $s0 and the base address of A is stored in $s6.
f = f + A[2];
Solution:
lw $t0, 8($s6) # $t0 <-- A[2]
add $s0, $s0, $t0 # f <-- f + A[2]

## Slide 6: Question 3: Branches and Jumps
Convert the following C code into MIPS assembly. Assume that the values of a, b, and i are in registers $s0, $s1, and $t0 respectively.
for (i=0; i<a; i++) a += b;

## Slide 7: Question 3: Branches and Jumps
Convert the following C code into MIPS assembly. Assume that the values of a, b, and i are in registers $s0, $s1, and $t0 respectively.
for (i=0; i<a; i++) a += b;
Solution:
addi $t0, $0, 0
j TEST
LOOP: add $s0, $s0, $s1
addi $t0, $t0, 1
TEST: slt $t2, $t0, $s0
bne $t2, $0, LOOP

## Slide 8: Question 4: Procedures
Convert the following C code into MIPS assembly.
int main() { int x = 10; int y = 20; int z; z = my_function(x, y, 100); } int my_function(int x, int y, int value) { return x – y + value; }

## Slide 9: Question 4: Procedures
Convert the following C code into MIPS assembly.
int main() { int x = 10; int y = 20; int z; z = my_function(x, y, 100); } int my_function(int x, int y, int value) { return x – y + value; }
Solution: Leaf Procedure (my_function)
FUNC: sub $t0, $a0, $a1
add $v0, $t0, $a3
jr $ra

## Slide 10: Question 4: Procedures
Solution: Non-Leaf Procedure (main)
MAIN: addi $sp, $sp, −4
sw $ra, ($sp)
addi $a0, $0, 10
addi $a1, $0, 20
addi $a3, $0, 100
jal FUNC
add $t2, $v0 $0
lw $ra, ($sp)
addi $sp, $sp, 4
jr $ra

## Slide 11: Question 5: Pointers
void copy (int a[], int b[], int n) { int i; for (i=0; i != n; i++) a[i] = b[i];
}
Translate this function into MIPS assembly.

## Slide 12: Question 5: Pointers
void copy (int a[], int b[], int n) { int i; for (i=0; i != n; i++) a[i] = b[i];
}
Assume the base address of a is in $a0, the base address of b is in $a1, and n is in $a2
copy: move $t0,$0
loop: beq $t0,$a2,done
sll $t1,$t0,2
add $t2,$t1,$a1
lw $t2,0($t2)
add $t1,$t1,$a0
sw $t2,0($t1)
addi $t0,$t0,1
j loop
done: jr $ra

## Slide 13: Question 5: Pointers
void copy (int a[], int b[], int n) { int i; for (i=0; i != n; i++) a[i] = b[i];
}
Convert this function into pointer-based C code.

## Slide 14: Question 5: Pointers
void copy (int a[], int b[], int n) { int i; for (i=0; i != n; i++) a[i] = b[i];
}
void copy(int *a, int *b, int n){
int *p,*q;
for(p=a,q=b;p!=a+n;p++,q++)
*p=*q;
}

## Slide 15: Question 5: Pointers
void copy(int *a, int *b, int n){
int *p,*q;
for(p=a,q=b;p!=a+n;p++,q++)
*p=*q;
}
Translate the pointer-based C code into assembly.

## Slide 16: Question 5: Pointers
void copy(int *a, int *b, int n){
int *p,*q;
for(p=a,q=b;p!=a+n;p++,q++)
*p=*q;
}
Assume the a, b and n are stored in $a0, $a1, and $a2 respectively.
copy: move $t0,$a0
move $t1,$a1
sll $t2,$a2,2
add $t2,$t2,$a0
loop: beq $t0,$t2,done
lw $t3,0($t1)
sw $t3,0($t0)
addi $t0,$t0,4
addi $t1,$t1,4
j loop
done: jr $ra

## Slide 17: Questions?