## Slide 1: CDA 3103
Recitation 1 – Number Conversions

## Slide 2: Converting: Binary to Decimal
Express the binary number, n, in the form: akbk + ak-1bk-1 + … + a1b + a0
Use 2 for b (the base is 2)
Fill in k
  Start with 0 for the least significant bit and count upward
Fill in ak
  These will be 0s or 1s
Solve the equation

## Slide 3: Converting: Decimal to Binary
Continually divide the decimal number by 2, recording the remainder each time, until 0 is reached. The remainders (read upwards from bottom to top) are the binary result.

## Slide 4: Question 1
Convert (11101011)2 to decimal.
akbk + ak-1bk-1 + … + a1b + a0
1*27 + 1*26 + 1*25 + 0*24 + 1*23 + 0*22 + 1*21 + 1*20
128 + 64 + 32 + 0 + 8 + 0 + 2 + 1
23510

## Slide 5: Question 2
Convert (937)10 to binary.
937 / 2 = 468 R 1
468 / 2 = 234 R 0
234 / 2 = 117 R 0
117 / 2 = 58 R 1
58 / 2 = 29 R 0
29 / 2 = 14 R 1
14 / 2 = 7 R 0
7 / 2 = 3 R 1
3 / 2 = 1 R 1
1 / 2 = 0 R 1
11101010012

## Slide 6: Signed Numbers: Sign and Magnitude Method
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–0
–1
–2
–3
–4
–5
–6
–7
0 100 = + 4 1 100 = – 4
The most significant bit is dedicated to sign
  sign: 0 = positive (or zero), 1 = negative
Other bits represent the absolute value or magnitude
  three low order bits: 0 (000) thru 7 (111)
Range for n bits
  There are two representations for 0
Cumbersome addition/subtraction
  must compare magnitudes to determine sign of result

## Slide 7: Signed Numbers: 1’s Complement Method
If N is a positive number, then the negative of N ( its 1’s complement or N' ) is
  Example: 1’s complement of 7
  Shortcut: simply compute bit-wise complement ( 0111 -> 1000 )
2 = 10000
1 = 00001
2 –1 = 1111
7 = 0111
1000 = –7 in 1s complement form
4
4

## Slide 8: Signed Numbers: 1’s Complement Method
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–7
–6
–5
–4
–3
–2
–1
–0
0 100 = + 4 1 011 = – 4
Subtraction implemented by 1’s complement and then addition
Two representations of 0
  Causes some complexities in addition
High-order bit can act as sign bit

## Slide 9: Signed Numbers: 2’s Complement Method
0 100 = + 4 1 100 = – 4
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
1’s complement with negative numbers shifted one position clockwise
  Only one representation for 0
  One more negative number than positive number
  High-order bit can act as sign bit

## Slide 10: Signed Numbers: 2’s Complement Method
If N is a positive number, then the negative of N ( its 2’s complement or N* ) is
  Example: 2’s complement of 7
  Example: 2’s complement of –7
  Shortcut: 2’s complement = bit-wise complement + 1
    0111 -> 1000 + 1 -> 1001 (representation of -7)
    1001 -> 0110 + 1 -> 0111 (representation of 7)
2 = 10000
7 = 0111
1001 = repr. of –7
4
2 = 10000
–7 = 1001
0111 = repr. of 7
4
subtract
subtract

## Slide 11: Summary: Binary, Signed Integer Representations
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
0
0
1
1
0
0
0
0
1
1
0
0
1
1
1
0
1
0
1
0
1
0
0
1
0
1
0
1
0
1
1
+
1
-
2
+
3
+
4
+
5
+
6
+
7
+
2
-
3
-
4
-
5
-
6
-
7
-
8
-
0
+
0
-
1
+
2
+
3
+
4
+
5
+
6
+
7
+
0
+
7
-
6
-
5
-
4
-
3
-
2
-
1
-
0
-
1
+
2
+
3
+
4
+
5
+
6
+
7
+
0
+
7
-
6
-
5
-
4
-
3
-
2
-
1
-
b
3
b
2
b
1
b
0
Sign and
magnitude
1'
s complement
2'
s complement
B
V
alues represented

## Slide 12: Question 3
Convert the binary number
1010 0100 1001 0010 0100 1001 0010 01002
to decimal, if the binary is
Unsigned?
2’s complement?

## Slide 13: Question 3.1
Converting binary (unsigned) to decimal
1010 0100 1001 0010 0100 1001 0010 01002
1*231 + 1*229 + … + 1*28 + 1*25 + 1*22
= 2761050404

## Slide 14: Question 3.2
Converting binary (2’s complement) to decimal
1010 0100 1001 0010 0100 1001 0010 01002
-1*231 + 1*229 + … + 1*28 + 1*25 + 1*22
= -1533916892

## Slide 15: Sign Extension
Suppose I have a 4-bit 2’s complement number and I want to make it into an 8-bit number
  Positive number
  – add 0’s to LHS e.g. 0111 -> 00000111
  Negative number
  – add 1’s to LHS e.g. 1010 -> 11111010

## Slide 16: Question 4
Add 0100 1111 and 1001, if they are
Unsigned?
2’s complement?

## Slide 17: Question 4.1
Add 0100 1111 and 1001, if they are unsigned
  Extend 1001 into an 8-bit number: 0000 1001
  Add 0100 1111
  0000 1001
  0101 1000

## Slide 18: Question 4.1
Add 0100 1111 and 1001, if they are 2’s complement
  Extend 1001 into an 8-bit number: 1111 1001
  Add 0100 1111
  1111 1001
  0100 1000