## Slide 1: CDA 3103
Recitation 7 – MIPS: Arithmetic, Branches, and Loops

## Slide 2: MIPS Architecture
MIPS (originally an acronym for Microprocessor without Interlocked Pipeline Stages) is a reduced instruction set computer (RISC) instruction set architecture (ISA)

## Slide 3: MIPS Architecture
Reduced instruction set computing, or RISC is a CPU design strategy based on the insight that simplified (as opposed to complex) instructions can provide higher performance if this simplicity enables much faster execution of each instruction

## Slide 4: MIPS Architecture
An instruction set, or instruction set architecture (ISA), is the part of the computer architecture related to programming.
It includes:
  native data types
  instructions
  registers
  addressing modes
  memory architecture
  interrupt and exception handling
  external I/O.
An ISA includes a specification of the set of opcodes (machine language), and the native commands implemented by a particular processor.

## Slide 5: MIPS Architecture
32-bit RISC Processor
32 32-bit Registers, $0..$31
All instructions are 32-bits
Most Instructions executed in one clock cycle
Byte addressable memory
  A 32-bit word contains four bytes
  To address the next word of memory add 4

## Slide 6: MIPS example
d = (a-b) + (a-c)
  Sub d,a,b # d=a-b
  Sub e,a,c # e=a-c
  Add d,d,e # d=d+e
Is this the best way?
Notes: Sub d,a,b ; add d,a,a; sub d,a,c -- no temp variable needed

## Slide 7: Registers
Special “addresses” where computation can take place
Hardware separate from memory, connected directly to ALU
MIPS registers are 32-bits, also called one word
MIPS has 32 registers

## Slide 8: Why Limit Number of Registers?
Each adds specialized hardware
  Additional cost (area, power)
More registers are slower
  Time for signal to travel…
More registers require bigger words
  More bits to represent register #

## Slide 9: Registers in MIPS Assembler
Each register has a name, beginning with $
Convention:
  $s0, $s1 … variables
  $t0, $t1 … temporary (intermediate values)

## Slide 10: Revised example
d = (a-b) + (a-c)
Assume $s0 = a, $s1 = b, $s2 = c, $s3 = d
Sub $t0, $s0, $s1
Sub $t1, $s0, $s2
Add $s3, $t0, $t1

## Slide 11: Try it!
Assume: a in $s0, b in $s1 c in $s2
a = (a + b) – (c + c)
Use only add and sub instructions

## Slide 12: Try it!
Assume: a in $s0, b in $s1 c in $s2
a = (a + b) – (c + c)
Use only add and sub instructions
add $t0, $s0, $s1
add $t1, $s2, $s2
sub $s0, $t0, $t1

## Slide 13: Moving Data Between Memory and Registers
Data (variables) stored in memory
Move to/from registers for computation
  “Load / Store word” (lw, sw) instructions
  Three operands:
    Destination register
    Offset (fixed value)
    Register (base address)

## Slide 14: Using Offset and Register
Offset is a fixed value, measured in bytes
Register’s value added to offset to compute the final address
Why?
  Register has more bits than offset
  Register contents can change during execution

## Slide 15: Realistic uses of base & register
A[j]
lw $t0, j*4( $s0 )
  offset = j*4
  Base register $s0 contains address of A

## Slide 16: Example
Given array A (address in $s0)
Goal: load A[1] into $t0
Instruction
  Lw $t0, 4 ($s0) # note 1 word = 4 bytes

## Slide 17: Another example
Addresses of A, B, C are in $s0+A, $s0+B, $s0+C ($s0 is beginning of “variable block”)
Compile: C = A+B
lw $t0, A($s0)
lw $t1, B($s0)
add $t0, $t0, $t1 #assume ok to reuse $t0
sw $t0, C($s0) #store value at C

## Slide 18: Try it!
Assume base of a is $s0, base of b is $s1, c is $s2
c = a[1]+b[1]

## Slide 19: Try it!
Assume base of a is $s0, base of b is $s1, c is $s2
c = a[1]+b[1]
lw $t0, 4($s0)
lw $t1, 4($s1)
add $s2, $t0, $t1

## Slide 20: Adding a constant…
To add a constant to a variable:
  A = A+4
  Lw $t0, 0($s0) # assume $s0 contains address of A
  Lw $t1, 0($s1) # assume $s1 contains address of a 4 in memory
  Add $t0, $t0, $t1
  Sw $t0, 0($s0)

## Slide 21: Disadvantages
All constants must be pre-stored in memory
Extra register used for each constant
Additional loads slow down the program

## Slide 22: Immediate Values
Use an “operand” slot for a small number rather than a register
The non-register operand is called “immediate”
Operations: Add immediate (addi)
Notes: How big a number can we have, if there are 32 registers? (+15, -16)

## Slide 23: Using Immediate Values
To add a constant to a variable:
  A = A+4
  lw $t0, 0($s0) # assume $s0 contains A
  addi $t0, $t0, 4
  sw $t0, 0($s0)

## Slide 24: MIPS machine language
Portions of the instruction are represented by binary numbers
  Operation code (opcode) = 12 bits
    6 at beginning (op); 6 at end (funct)
  Registers (32 possible) = 5 bits each
    $s0 = 16 … $s7 = 23, $t0 = 8 … $t7 = 15
  Not yet used field = 5 bits

## Slide 25: ADD $t0,$s1,$s2 instruction
000000 10001 10010 01000 00000 100000
  000000 (operation = 0) “op”
  10001 (register 17 = $s1) “rs” register source 1
  10010 (register 18 = $s2) “rt” register source 2
  01000 (register 8 = $t0) “rd” register destination
  00000 (unused field) “shamt” shift amount
  100000 (function = 32) “funct”
Hex representation: 02324020

## Slide 26: Format for Immediate
Immediate operations also 32 bits
Instead of 3 registers, we have 2 registers + an immediate field
  If we used only one register’s bits, we could have only 32 immediate values
  Use all remaining 16 bits (rd, shamt, func) for immediate value
    How many values can we have now?

## Slide 27: Summary of Instruction Formats (so far)
R-type (register)
  Op(6), rs(5), rt(5), rd(5), shamt(5), funct(6)
I-type (immediate)
  Op(6), rs(5), rt(5), constant or address (16)
  Used for immediate instructions and also load/store
  Register rt is source for sw, dest for lw, addi, etc.

## Slide 28: Logical Operations
Shift
  Shifts bits to left or right, filling in with 0’s
  sll (shift left logical)
  srl (shift right logical)
Bitwise logical
  And, andi rd = rs & rt
  Or, ori rd = rs | rt
  Nor rd = ! (rs | rt)

## Slide 29: Examples
Sll $t2, $s0, 4
  Shift $s0 left by 4 bits & put result in $t2
  Effectively multiplies $s0 by 2^4
And $t2, $s0, $s1
  $t2 has 1 only when both $s0 and $s1 have 1 in corresponding bit (otherwise 0)
Ori $t2, $s0, 15
  Copies $s0 into $t2 except sets the last 4 bits to 1 (because of OR with 000….1111)
Nor $t2, $t1, $zero # $zero is a reg. fixed to 0
  $t2 gets not $t1
Notes: Nori is almost always used for not and we have $zero, therefore, no nori is implemented

## Slide 30: Control Structures
The only control structures are jumps (also called branches in MIPS)
Conditional branches:
  Beq reg1, reg2, addr (branch on equal)
  Bne reg1, reg2, addr (branch not equal)
Unconditional jump:
  J addr

## Slide 31: IF Example
#if (a == 0) a=a+c else a=a+b
#a is in $s0, b is in $s1, c is in $2
bne $s0, $zero, ELSE
add $s0, $s0, $s2 #we will add c
j DONE
ELSE: add $s0, $s0, $s1 #we will add b
DONE:

## Slide 32: Loops
While loop (test at top)
  Conditional branch at beginning (to jump beyond the loop)
  Unconditional branch at end (to return to the top)
Until loop (test at end)
  Conditional branch at bottom
  Loop body executes at least once

## Slide 33: Try it!
//Assume sum = sum($s0), val = val($s0), N = N($s0)
int sum = 0;
int val = 0;
while (val != N){
  sum = sum + val;
  val++;}

## Slide 34: Try it!
//Assume sum is in $s0, val is in $s1, and N is in $s3
int sum = 0;
int val = 0;
while (val != N){
  sum = sum + val;
  val++;}
add $s0, $zero, $zero
add $s1, $zero, $zero
LOOP: beq $s1, $s3, DONE
add $s0, $s0, $s1
addi $s1, $s1, 1
j LOOP
DONE:

## Slide 35: Testing for inequality
First set a register with a flag based on comparison
  slt $t0, $s1, $s2 (t0=1 if s1<s2, else 0)
  slti $t0, $s1, 1 (t0=1 if s1<1, else 0)
Next, use beq or bne as appropriate
  beq $t0, $zero (branch if s1>=s2)
  bne $t0, $zero (branch if s1< s2)
Notes: How to branch if s1>s2 or s1<=s2? (reverse order of args to slt)
Note pseudoInstructions: blt ,bgt, ble ,bge -> each maps to a pair of real instructions, e.g. blt $s0, $s1, LABEL = slt $t0, $s0, $s1 ; bne $t0, $zero, LABEL

## Slide 36: Case / Switch statement
First create an array of possible locations to jump to
This is the jump address table
Next, jump to the right value in the table

## Slide 37: Switch example:
switch(x){
case 0: a=b&c; break;
case 1: a=b+c; break;
case 2: a= b-c; break;
}
Contents of jumptable:
AND
PLUS
MINUS

## Slide 38: Switch Example continued
switch(x){
case 0:
a=b&c;
break;
case 1:
a=b+c;
break;
case 2:
a= b-c;
break;
}
# Assume x in $s0, a in $s1,
# b in $s2, c in $s3, and
# address for jumptable in $s4
sll $t0, $s0, 2 # multiply x by 4 for address
add $t1, $t0, $s4 #use x as offset
jr $t1 #t1 is jumptable + x
AND: and $s1,$s2,$s3
J DONE
PLUS: add $s1, $s2, $s3
J DONE
MINUS: sub $s1, $s2, $s3
DONE:

## Slide 39: Questions?