## Slide 1: CDA 3103
Recitation 6 – Floating Point Numbers and Operations

## Slide 2: Parts of a Floating Point Number
-0.9876 x 10-3
Sign of mantissa
Location of decimal point
Mantissa
Exponent
Sign of exponent
Base

## Slide 3: Single Precision Format
32 bits
Mantissa (23 bits)
Exponent (8 bits)
Sign of mantissa (1 bit)

## Slide 4: Normalization
The mantissa is normalized
Has an implied decimal place on left
Has an implied “1” on left of the decimal place
E.g.,
  Mantissa 
  Represents…
10100000000000000000000
1.1012 = 1.62510

## Slide 5: Excess Notation
To include +ve and –ve exponents, “excess” notation is used
Single precision: excess 127
Double precision: excess 1023
The value of the exponent stored is larger than the actual exponent
E.g., excess 127,
  Exponent 
  Represents…
10000111
135 – 127 = 8

## Slide 6: Question 1
Convert the binary number
1010 0100 1001 0010 0100 1001 0010 01002
to decimal, if the binary represents a single precision floating-point value?

## Slide 7: Question 1
Converting binary (Single precision FP) to decimal.
1010 0100 1001 0010 0100 1001 0010 01002
Sign bit: 1
Exponent: 01001001 = 73
Fraction: 00100100100100100100100
=1*2-3 + 1*2-6 + … + 1*2-15 + 1*2-18 + 1*2-21
=0.142857074
S(1)
Biased Exponent(8)
Fraction (23)

## Slide 8: Question 1
Converting binary (Single precision FP) to decimal.
1010 0100 1001 0010 0100 1001 0010 01002
(-1)S * (1.Fraction) * 2(Exponent - 127)
=(-1)1 * (1.142857074) * 2(73 - 127)
=-1.142857074 * 2-54
=-6.344131187 * 10-17
S(1)
Biased Exponent(8)
Fraction (23)

## Slide 9: Question 2
Show the IEEE 754 binary representation for the floating-point number 0.110 in single­ precision.

## Slide 10: Question 2
Converting 0.110 to single-precision FP
Step 1: Convert fraction 0.1 to binary (multiplying by 2)
0.1*2 = 0.2 0.2*2 = 0.4 0.4*2 = 0.8 0.8*2 = 1.6 0.6*2 = 1.2 0.2*2 = 0.4 0.4*2 = 0.8
0.8*2 = 1.6 0.6*2 = 1.2
000110011…
(The pattern 0011 repeats)

## Slide 11: Question 2
Converting 0.110 to single-precision FP
Step 2: Normalize
000110011…
1.10011… * 2-4

## Slide 12: Question 2
Converting 0.110 to single-precision FP
Step 3: Determine S, E, and M
S = 0 E = -4 + 127
= 123 = 01111011
M = 10011001100110011001100

## Slide 13: Question 2
Converting 0.110 to single-precision FP
Step 4: Express in single precision format
0
01111011
10011001100110011001100

## Slide 14: Question 3
Convert the following single-precision number into decimal
0111 1111 1000 0000 0000 0000 000 0000

## Slide 15: Question 3
Converting binary (Single precision FP) to decimal
0 11111111 000000000000000000000002
Sign bit : 0
Exponent : 11111111 = Infinity
Fraction : 00000000000000000000000 = 0
Infinity
S(1)
Biased Exponent(8)
Fraction (23)

## Slide 16: Question 4
Add the following two single precision FP values
0100 0001 0111 1011 0000 0000 0000 0000
0100 0010 0111 0101 0000 0000 0000 0000

## Slide 17: Question 4
0100 0001 0111 1011 0000 0000 0000 0000 +
0100 0010 0111 0101 0000 0000 0000 0000
Express values in scientific notation
  0 10000010 11110110000000000000000
  = 1.1111011 * 2(130-127) = 1.1111011* 23
  0 10000100 11101010000000000000000
  =1.1110101* 2(132-127) = 1.1110101* 25

## Slide 18: Question 4
0100 0001 0111 1011 0000 0000 0000 0000 +
0100 0010 0111 0101 0000 0000 0000 0000
Denormalize smaller value
  1.1111011* 23
  = .011111011 * 25

## Slide 19: Question 4
0100 0001 0111 1011 0000 0000 0000 0000 +
0100 0010 0111 0101 0000 0000 0000 0000
Add aligned components
  1.1110101 * 25
  + .011111011 * 25
  = 10.011001111 * 25

## Slide 20: Question 4
0100 0001 0111 1011 0000 0000 0000 0000 +
0100 0010 0111 0101 0000 0000 0000 0000
Normalize sum
  10.011001111 * 25
  = 1.0011001111 * 26

## Slide 21: Question 5
Multiply the following two single precision FP values
0100 0001 0111 1011 0000 0000 0000 0000
0100 0010 0111 0101 0000 0000 0000 0000

## Slide 22: Question 5
0100 0001 0111 1011 0000 0000 0000 0000 *
0100 0010 0111 0101 0000 0000 0000 0000
Express values in normalized scientific notation
  0 10000010 11110110000000000000000
  = 1.1111011 * 2(130-127) = 1.1111011* 23
  0 10000100 11101010000000000000000
  =1.1110101* 2(132-127) = 1.1110101* 25

## Slide 23: Question 5
0100 0001 0111 1011 0000 0000 0000 0000 *
0100 0010 0111 0101 0000 0000 0000 0000
Denormalize values
  1111 1011* 2-4
  1111 0101* 2-2

## Slide 24: Question 5
0100 0001 0111 1011 0000 0000 0000 0000 *
0100 0010 0111 0101 0000 0000 0000 0000
Compute Exponent
  1111 1011* 2-4
  1111 0101* 2-2
  Exp = -4 + -2 = -6

## Slide 25: Question 5
0100 0001 0111 1011 0000 0000 0000 0000 *
0100 0010 0111 0101 0000 0000 0000 0000
Multiply Significands
  1 1 1 1 1 0 1 1
  1 1 1 1 0 1 0 1 1 1 1 1 1 0 1 1 0 0 0 0 0 0 0 0 1 1 1 1 1 0 1 1
  0 0 0 0 0 0 0 0
  1 1 1 1 1 0 1 1
  1 1 1 1 1 0 1 1
  1 1 1 1 1 0 1 1
  1 1 1 1 1 0 1 1
  1 1 1 1 0 0 0 0 0 0 1 1 0 1 1 1

## Slide 26: Question 5
0100 0001 0111 1011 0000 0000 0000 0000 *
0100 0010 0111 0101 0000 0000 0000 0000
Normalize product
  1111 0000 0011 0111
  1111 0000 0011 0111 * 2-6
  1.111000000110111 * 29