## Slide 1: CDA 3103
Recitation 5 – Booth’s Algorithm and Binary Integer Division

## Slide 2: Booth's Algorithm Example

## Slide 3: Points to remember
When using Booth's Algorithm:
  You will need twice as many bits in your product as you have in your original two operands.
  The leftmost bit of your operands (both your multiplicand and multiplier) is a SIGN bit, and cannot be used as part of the value.

## Slide 4: To begin
Decide which operand will be the multiplier and which will be the multiplicand
Convert both operands to two's complement representation using X bits
  X must be at least one more bit than is required for the binary representation of the numerically larger operand
Begin with a product that consists of the multiplier with an additional X leading zero bits

## Slide 5: Example
For our example, let's multiply (-5) x 2
  The numerically larger operand (5) would require 3 bits to represent in binary (101). So we must use AT LEAST 4 bits to represent the operands, to allow for the sign bit.
Let's use 5-bit 2's complement:
  -5 is 11011 (multiplier)
  2 is 00010 (multiplicand)

## Slide 6: Beginning Product
The multiplier is:
11011
Add 5 leading zeros to the multiplier to get the beginning product:
00000 11011

## Slide 7: Step 1 for each pass
Use the LSB (least significant bit) and the previous LSB to determine the arithmetic action.
  If it is the FIRST pass, use 0 as the previous LSB.
Possible arithmetic actions:
  00  no arithmetic operation
  01  add multiplicand to left half of product
  10  subtract multiplicand from left half of product
  11  no arithmetic operation

## Slide 8: Step 2 for each pass
Perform an arithmetic right shift (ASR) on the entire product.
NOTE: For X-bit operands, Booth's algorithm requires X passes.

## Slide 9: Example
Let's continue with our example of multiplying (-5) x 2
Remember:
  -5 is 11011 (multiplier)
  2 is 00010 (multiplicand)
And we added 5 leading zeros to the multiplier to get the beginning product:
00000 11011

## Slide 10: Example continued
Initial Product and previous LSB
00000 11011 0
(Note: Since this is the first pass, we use 0 for the previous LSB)
Pass 1, Step 1: Examine the last 2 bits
00000 11011 0
The last two bits are 10, so we need to:
subtract the multiplicand from left half of product

## Slide 11: Example: Pass 1 continued
Pass 1, Step 1: Arithmetic action
(1) 00000 (left half of product)
-00010 (mulitplicand)
11110 (uses a phantom borrow)
Place result into left half of product
11110 11011 0

## Slide 12: Example: Pass 1 continued
Pass 1, Step 2: Arithmetic Shift Right
  Before ASR
  11110 11011 0
  After ASR
  11111 01101 1
  (left-most bit was 1, so a 1 was shifted in on the left)
Pass 1 is complete.

## Slide 13: Example: Pass 2
Current Product and previous LSB
11111 01101 1
Pass 2, Step 1: Examine the last 2 bits
11111 01101 1
The last two bits are 11, so we do NOT need to perform an arithmetic action -- just proceed to step 2.

## Slide 14: Example: Pass 2 continued
Pass 2, Step 2: ASR (arithmetic shift right)
  Before ASR
  11111 01101 1
  After ASR
  11111 10110 1
  (left-most bit was 1, so a 1 was shifted in on the left)
Pass 2 is complete.

## Slide 15: Example: Pass 3
Current Product and previous LSB
11111 10110 1
Pass 3, Step 1: Examine the last 2 bits
11111 10110 1
The last two bits are 01, so we need to: add the multiplicand to the left half of the product

## Slide 16: Example: Pass 3 continued
Pass 3, Step 1: Arithmetic action
(1) 11111 (left half of product)
+00010 (mulitplicand)
00001 (drop the leftmost carry)
Place result into left half of product
00001 10110 1

## Slide 17: Example: Pass 3 continued
Pass 3, Step 2: ASR (arithmetic shift right)
  Before ASR
  00001 10110 1
  After ASR
  00000 11011 0
  (left-most bit was 0, so a 0 was shifted in on the left)
Pass 3 is complete.

## Slide 18: Example: Pass 4
Current Product and previous LSB
00000 11011 0
Pass 4, Step 1: Examine the last 2 bits
00000 11011 0
The last two bits are 10, so we need to: subtract the multiplicand from the left half of the product

## Slide 19: Example: Pass 4 continued
Pass 4, Step 1: Arithmetic action
(1) 00000 (left half of product)
-00010 (mulitplicand)
11110 (uses a phantom borrow)
Place result into left half of product
11110 11011 0

## Slide 20: Example: Pass 4 continued
Pass 4, Step 2: ASR (arithmetic shift right)
  Before ASR
  11110 11011 0
  After ASR
  11111 01101 1
  (left-most bit was 1, so a 1 was shifted in on the left)
Pass 4 is complete.

## Slide 21: Example: Pass 5
Current Product and previous LSB
11111 01101 1
Pass 5, Step 1: Examine the last 2 bits
11111 01101 1
The last two bits are 11, so we do NOT need to perform an arithmetic action -- just proceed to step 2.

## Slide 22: Example: Pass 5 continued
Pass 5, Step 2: ASR (arithmetic shift right)
  Before ASR
  11111 01101 1
  After ASR
  11111 10110 1
  (left-most bit was 1, so a 1 was shifted in on the left)
Pass 5 is complete.

## Slide 23: Final Product
We have completed 5 passes on the 5-bit operands, so we are done.
Dropping the previous LSB, the resulting final product is:
11111 10110

## Slide 24: Verification
To confirm we have the correct answer, convert the 2's complement final product back to decimal.
Final product: 11111 10110
Decimal value: -10
which is the CORRECT product of:
  (-5) x 2

## Slide 25: Binary Integer Division

## Slide 26: Signed Division
For our example, we will calculate 15 / -3
Store the signs of the divisor and dividend
Convert negative values to positive
Complement quotient and remainder if necessary
  Dividend and Remainder are defined to have same sign
  Quotient negated if Divisor sign and Dividend sign disagree

## Slide 27: Example
Using 5-bit 2’s Complement values:
  15 = 01111
  -3 = 11101
Convert divisor to positive:
  3 = 00011

## Slide 28: For each Pass
Subtract the divisor from the left half of the remainder and place the result in the left half of the remainder
If the remainder is positive
  Shift the remainder to the left, shifting in a 1
If the remainder is negative
  Restore the previous remainder
  Shift to the remainder to the left, shifting in a 0

## Slide 29: Example
Dividend = 01111 (15)
Divisor = 00011 (3)
-Divisor = 11101 (-3)
Initialize:
  Remainder: 00000 01111
  Shift remainder left 1 bit: 00000 11110

## Slide 30: Example, Pass 1
Subtract the divisor from the left half of the remainder
  00000 (left half of the remainder)
  + 11101 (negative form of divisor)
  11101
Place result into left half of product
11101 11110

## Slide 31: Example, Pass 1
Check to see if the remainder is negative or positive
11101 11110
Starts with a 1 – therefore negative
Restore previous value
00000 11110
shift to the left, shift in 0
00001 11100

## Slide 32: Example, Pass 2
Subtract the divisor from the left half of the remainder
  00001 (left half of the remainder)
  + 11101 (negative form of divisor)
  11110
Place result into left half of product
11110 11100

## Slide 33: Example, Pass 2
Check to see if the remainder is negative or positive
11110 11100
Starts with a 1 – therefore negative
Restore previous value
00001 11100
shift to the left, shift in 0
00011 11000

## Slide 34: Example, Pass 3
Subtract the divisor from the left half of the remainder
  00011 (left half of the remainder)
  + 11101 (negative form of divisor)
  00000
Place result into left half of product
00000 11000

## Slide 35: Example, Pass 3
Check to see if the remainder is negative or positive
00000 11000
Starts with a 0 – therefore positive
shift to the left, shift in 1
00001 10001

## Slide 36: Example, Pass 4
Subtract the divisor from the left half of the remainder
  00001 (left half of the remainder)
  + 11101 (negative form of divisor)
  11110
Place result into left half of product
11110 10001

## Slide 37: Example, Pass 4
Check to see if the remainder is negative or positive
11110 10001
Starts with a 1 – therefore negative
Restore previous value
00001 10001
shift to the left, shift in 0
00011 00010

## Slide 38: Example, Pass 5
Subtract the divisor from the left half of the remainder
  00011 (left half of the remainder)
  + 11101 (negative form of divisor)
  00000
Place result into left half of product
00000 00010

## Slide 39: Example, Pass 5
Check to see if the remainder is negative or positive
00000 00010
Starts with a 0 – therefore positive
shift to the left, shift in 1
00000 00101

## Slide 40: To Finish
Shift the left half of the remainder to the right 1 bit
00000 00101
Set sign bits
Remainder is zero
Need to negate quotient because divisor (-) and dividend (+) have differing signs
  00101 => 11011

## Slide 41: Final Result
We have completed 5 passes on the 5-bit operands, so we are done.
The resulting final quotient is 11011
The resulting final remainder is 00000

## Slide 42: Verification
To confirm we have the correct answer, convert the 2's complement quotient back to decimal.
Quotient: 11011
Decimal value: -5
which is the CORRECT result of:
  15 / -3