## Slide 1: Performance

## Slide 2: Introduction
The performance of a system depends on:
  algorithms
  programming language
  architecture
  hardware elements
Assessing performance can be challenging

## Slide 3: Introduction
What is performance?
Airplane | Passengers | Range | Speed | Throughput
Boeing 747 | 470 | 4150 | 610 | 286,700
Concorde | 132 | 4000 | 1350 | 178,200
DC-8-50 | 146 | 8720 | 544 | 79.424

## Slide 4: Definitions of Performance
Response time
  How long it takes to do a task
    Execution time
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour

## Slide 5: Performance as Response Time
To increase performance, reduce response time.
“X is n time faster than Y”
Performance(X) Execution Time(Y)
–––––––––––––– = –––––––––––––––– = n
Performance(Y) Execution Time(X)
1
Performance(X) = ––––––––––––––––
Execution Time(X)

## Slide 6: Example
If computer A runs a program in 10 seconds and computer B runs the same program in 15 seconds, how much faster is A than B?
A is 1.5 times faster than B.
Execution Time(B) 15
–––––––––––––– = –––––––––––––––– = n
Execution Time(A) 10
Execution Time(B) 15
–––––––––––––– = –––––––––––––––– = 1.5
Execution Time(A) 10
Performance(A) Execution Time(B)
–––––––––––––– = –––––––––––––––– = n
Performance(B) Execution Time(A)

## Slide 7: Measuring Performance
Time is our metric for determining performance
Time can be defined in different ways

## Slide 8: Measuring Execution Time
Elapsed time
  “Wall-clock” time, Response time
  Total time to complete task, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance
CPU Performance
System Performance

## Slide 9: CPU Clocking
Clock period: duration of a clock cycle
  e.g. 250 ps
Clock frequency: cycles per second
  e.g. 4 GHz
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 10: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Trade-offs:
    Designers often trade off clock rate against cycle count
CPU Time = CPU Clock Cycles x Clock Cycle Time

## Slide 11: Example
Our favorite program runs in 10 seconds on computer A, which has a 4 GHz clock. We are trying to help a computer designer build a computer, B, that will run this program in 6 seconds.
The designer has determined that a substantial increase in the clock rate is possible, but this increase will affect the rest of the CPU design, causing computer B to require 1.2 times as many clock cycles as computer A for this program.
What clock rate should we tell the designer to target?

## Slide 12: CPU Time Example
Computer A: 4GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?
CPU clock cycles
CPU Time = ––––––––––––––––
Clock rate
CPU clock cycles A
10s = ––––––––––––––––
4 GHz
CPU clock cycles A = 10 * 4 GHz
Clock rate (B) = 8 GHz
1.2 * CPU clock cycles A
6s = ––––––––––––––––
Clock rate (B)
1.2 * 10 * 4 Ghz
Clock rate(B) = ––––––––––––––––
6

## Slide 13: Instructions
Execution time also depends on the number of instructions in a program
Clock cycles Per Instruction (CPI) is an average measurement.
  Different instructions might take a different number of cycles
  Determined by CPU hardware
  Affected by instruction mix
CPU Clock Cycles = Instruction Count x Cycles Per Instruction

## Slide 14: Example
Suppose we have two implementations of the same instruction set architecture. Computer A has a clock cycle time of 250 ps and a CPI of 2.0 for some program, and computer B has a clock cycle time of 500 ps and a CPI of 1.2 for the same program.
Which computer is faster for this program, and by how much?

## Slide 15: Example
Computer A
  clock cycle time of 250 ps
  CPI of 2.0
Computer B
  clock cycle time of 500 ps
  CPI of 1.2
CPU clock cycles of A = I * 2.0
CPU clock cycles of B = I * 1.2
CPU Time(A) = CPU clock cycles of A * clock cycle time of A
= I * 2.0 * 250 ps
= I * 500 ps
CPU Time(B) = CPU clock cycles of B * clock cycle time of B
= I * 1.2 * 500 ps
= I * 600 ps

## Slide 16: Example
Computer A
  clock cycle time of 250 ps
  CPI of 2.0
Computer B
  clock cycle time of 500 ps
  CPI of 1.2
CPU clock cycles of A = I * 2.0
CPU clock cycles of B = I * 1.2
CPU Time(A) = I * 500 ps
CPU Time(B) = I * 600 ps
Performance(A) Execution Time(B) I*600 ps
–––––––––––––– = –––––––––––––––– = ––––––––– = 1.2
Performance(B) Execution Time(A) I * 500 ps

## Slide 17: CPU Performance Equation
CPU Time = Instruction Count x CPI x Clock Cycle

## Slide 18: Components of Performance
Instr Count CPI Clock Rate
(IC) (CR)
Program X
Compiler X
ISA X X X
Organization X X
Technology X X
CPU Time = Instruction Count x CPI x Clock Cycle

## Slide 19: Components of Performance
CPU Time
  measure the time it takes to run the program
Clock Cycle
  usually published as part of the computer’s documentation
Instruction Count
  software tools that profile execution
  hardware counters
CPI
  average number of clock cycles
  affected by the instruction mix: the frequency of occurrence for instruction types and the clock cycles for instruction types
CPU Time = Instruction Count x CPI x Clock Cycle

## Slide 20: CPI in More Detail
If Pi is the probability of instruction type i and CPIi is the cycles taken by an instruction of type i, then

## Slide 21: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 22: Using the CPU Performance Equation
Here is the standard mix of instruction types in MIPS
Average CPI = 1.6
Instruction Type | Frequency | Cycles | MIPS CPI
Load | 30% | 2 | .6
Store | 15% | 2 | .3
A/L | 40% | 1 | .4
Branch | 15% | 2 | .3

## Slide 23: Using the CPU Performance Equation
Suppose we added a new instruction type. A/L-mem instructions can have one memory operand (eliminates the load+A/L operation combo).
We call the new instruction mix MIPS-E
A/L-mem operations take 2 clock cycles
A/L-mem replace half of load operations and a corresponding number of A/L operations
If the clock cycle period for a MIPS-E processor is 1.25 times that of a MIPS processor, which is faster?

## Slide 24: Solution 1
Calculate the IC, CPI, and CC of MIPS-E
MIPS-E IC:
  ICMIPS-E = ICMIPS – instrs replaced + instrs added = ICMIPS + (-(0.5 X 30% X 2)+0.5 X 30%) X ICMIPS = ICMIPS – 0.15 X ICMIPS = 0.85 X ICMIPS

## Slide 25: Solution 1
Calculate the IC, CPI, and CC of MIPS-E
MIPS-E IC: 0.85 X ICMIPS
MIPS-E CPI: 1.45 / .85 = 1.7
Instruction Type | Frequency | Cycles | MIPS CPI
Load | 15% | 2 | .3
Store | 15% | 2 | .3
A/L | 25% | 1 | .25
Branch | 15% | 2 | .3
A/L-mem | 15% | 2 | .3

## Slide 26: Solution 1
Calculate the IC, CPI, and CC of MIPS-E
MIPS-E IC: 0.85 X ICMIPS
MIPS-E CPI: 1.7
MIPS-E CC: 1.25 X CCMIPS

## Slide 27: Solution 1
Calculate the IC, CPI, and CC of MIPS-E
MIPS-E IC: 0.85 X ICMIPS
MIPS-E CPI: 1.7
MIPS-E CC: 1.25 X CCMIPS
CPU Time(MIPS) = 1.6 X ICMIPS X CCMIPS
CPU Time(MIPS-E) = 1.7 X .85 X ICMIPS X 1.25 X CCMIPS
= 1.8 X ICMIPS X CCMIPS

## Slide 28: Solution 1
Calculate the IC, CPI, and CC of MIPS-E
MIPS-E IC: 0.85 X ICMIPS
MIPS-E CPI: 1.7
MIPS-E CC: 1.25 X CCMIPS
CPU Time(MIPS) = 1.6 X ICMIPS X CCMIPS
CPU Time(MIPS-E) = 1.8 X ICMIPS X CCMIPS
MIPS processor is faster
Perf (MIPS) ET(MIPS-E) 1.8 X IC X CC
––––––––– = –––––––––– = –––––––––––– = 1.13
Perf (MIPS-E) ET (MIPS) 1.6 X IC X CC

## Slide 29: Solution 2
Calculate CPU cycles of MIPS-E
CyclesMIPS = ICMIPS X CPIMIPS = 1.6 X ICMIPS
CyclesMIPSE = CyclesMIPS – saved + added
saved = load cycles saved + ALU cycles saved = (30% X 0.5 X 2 + 30% X 0.5 X 1) X ICMIPS = 0.45 X ICMIPS
added = ALU-memory instruction cycles = (30% X 0.5 X 2) X ICMIPS = 0.3 X ICMIPS
CyclesMIPSE = CyclesMIPS – .45 X ICMIPS + 0.3 X ICMIPS = 1.6 X ICMIPS – 0.15 X ICMIPS = 1.45 X ICMIPS

## Slide 30: Solution 2
Calculate CPU cycles of MIPS-E
CyclesMIPS = 1.6 X ICMIPS
CyclesMIPSE = 1.45 X ICMIPS

## Slide 31: Solution 2
Calculate CPU cycles of MIPS-E
CyclesMIPS = 1.6 X ICMIPS
CyclesMIPSE = 1.45 X ICMIPS
CPU Time(MIPS) = 1.6 X ICMIPS X CCMIPS
CPU Time(MIPS-E) = 1.45 X ICMIPS X 1.25 x CCMIPS
= 1.81 X ICMIPS X CCMIPS

## Slide 32: Solution 2
Calculate CPU cycles of MIPS-E
CyclesMIPS = 1.6 X ICMIPS
CyclesMIPSE = 1.45 X ICMIPS
CPU Time(MIPS) = 1.6 X ICMIPS X CCMIPS
CPU Time(MIPS-E) = 1.45 X ICMIPS X 1.25 x CCMIPS
= 1.81 X ICMIPS X CCMIPS
MIPS processor is faster
Perf (MIPS) ET(MIPS-E) 1.81 X IC X CC
––––––––– = –––––––––– = –––––––––––– = 1.13
Perf (MIPS-E) ET (MIPS) 1.6 X IC X CC

## Slide 33: Solution 3
Normalize instruction sets
CPU Time(MIPS) = 160 cycles X CCMIPS
CPU Time(MIPS-E) = 145 cycles X 1.25 x CCMIPS
Instruction | CPI | IC | Cycles | Changes | IC | Cycles
Load | 2 | 30 | 60 | -15 | 15 | 30
Store | 2 | 15 | 30 |  | 15 | 30
A/L | 1 | 40 | 40 | -15 | 25 | 25
Branch | 2 | 15 | 30 |  | 15 | 30
A/L-mem | 2 | 0 | 0 | +15 | 15 | 30
Total |  | 100 | 160 |  | 85 | 145

## Slide 34: Solution 3
Normalize instruction sets
CPU Time(MIPS) = 160 cycles X CCMIPS
CPU Time(MIPS-E) = 145 cycles X 1.25 x CCMIPS
MIPS processor is faster
Perf (MIPS) ET(MIPS-E) 181.25 cycles X CC
––––––––– = –––––––––– = –––––––––––– = 1.13
Perf (MIPS-E) ET (MIPS) 160 cycles X CC

## Slide 35: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, CC

## Slide 36: Single-Cycle Datapath
Operation times for functional units:
  Memory: 200 ps
  ALU: 100 ps
  Registers: 50 ps
Which is faster?
  An implementation in which every instruction operates in 1 clock cycle of a fixed length.
  An implementation where every instruction executes in 1 clock cycle using a variable-length clock, which for each instruction is only as long as it needs to be.
Assume: 25% loads, 10% stores, 45% A/L, 15% branches, 5% jumps

## Slide 37: Single-Cycle Datapath
  An implementation in which every instruction operates in 1 clock cycle of a fixed length.
  An implementation where every instruction executes in 1 clock cycle using a variable-length clock, which for each instruction is only as long as it needs to be.
  CPI must be 1
  How long should the clock cycle time be?
CPU Time = Instruction Count x CPI x Clock Cycle

## Slide 38: Single-Cycle Datapath
Compute the required length for each instruction:
Instruction Type | Functional units used by instructions |  |  |  | 
A/L | Instruction Memory | Register | ALU | Register | 
Load | Instruction Memory | Register | ALU | Data Memory | Register
Store | Instruction Memory | Register | ALU | Data Memory | 
Branch | Instruction Memory | Register | ALU |  | 
Jump | Instruction Memory |  |  |  | 

## Slide 39: Single-Cycle Datapath
Compute the required length for each instruction:
CPU Time(single clock) = IC * 600
Instruction Type | Instruction Memory | Register | ALU | Data Memory | Register | Total
A/L | 200 | 50 | 100 | 0 | 50 | 400
Load | 200 | 50 | 100 | 200 | 50 | 600
Store | 200 | 50 | 100 | 200 | 0 | 550
Branch | 200 | 50 | 100 | 0 | 0 | 350
Jump | 200 | 0 | 0 | 0 | 0 | 200

## Slide 40: Single-Cycle Datapath
Compute the required length for each instruction:
Cycle Time (variable clock) = 600 X 25% + 550 X 10% + 400 X 45% + 350 X 15% + 200 X 5% = 447.5 ps
Instruction Type | Instruction Memory | Register | ALU | Data Memory | Register | Total
A/L | 200 | 50 | 100 | 0 | 50 | 400
Load | 200 | 50 | 100 | 200 | 50 | 600
Store | 200 | 50 | 100 | 200 | 0 | 550
Branch | 200 | 50 | 100 | 0 | 0 | 350
Jump | 200 | 0 | 0 | 0 | 0 | 200

## Slide 41: Single-Cycle Datapath
Compute the required length for each instruction:
CPU Time(single clock) = IC * 600
CPU Time(variable clock) = IC * 447.5
Instruction Type | Instruction Memory | Register | ALU | Data Memory | Register | Total
A/L | 200 | 50 | 100 | 0 | 50 | 400
Load | 200 | 50 | 100 | 200 | 50 | 600
Store | 200 | 50 | 100 | 200 | 0 | 550
Branch | 200 | 50 | 100 | 0 | 0 | 350
Jump | 200 | 0 | 0 | 0 | 0 | 200

## Slide 42: Single-Cycle Datapath
The variable clock implementation is faster.
Why don’t we use variable clocks?
  Too difficult
  Overhead outweighs potential speedup
Perf (variable) ET(single) 600
––––––––– = –––––––––– = ––––– = 1.34
Perf (single) ET (variable) 447.5

## Slide 43: Pipelined Datapath
Compare the throughput of three load instructions on a single-cycle processor to a pipelined processor.
Instructions take 600 ps to complete in the single cycle datapath.

## Slide 44: Pipelined Datapath
Each functional unit belongs to a different stage
Each stage requires one clock cycle to complete.
The clock cycle time must at least as long as the longest stage.
  200 ps.
Instruction Type | Instruction Memory | Register | ALU | Data Memory | Register | Total
A/L | 200 | 50 | 100 | 0 | 50 | 400
Load | 200 | 50 | 100 | 200 | 50 | 600
Store | 200 | 50 | 100 | 200 | 0 | 550
Branch | 200 | 50 | 100 | 0 | 0 | 350
Jump | 200 | 0 | 0 | 0 | 0 | 200

## Slide 45: Single-Cycle vs. Pipelined
1800 ps total
1400 ps total

## Slide 46: Single-Cycle vs. Pipelined
The pipelined approach is faster.
Perf (pipeline) ET(single) 1800
––––––––– = –––––––––– = ––––– = 1.28
Perf (single) ET (pipeline) 1400

## Slide 47: Benchmarks
Someone who uses the same programs day after day are good candidates for measuring computer performance
  Use the same programs on two computers
  Compare execution times of the same workload
Benchmarks simulate standard workloads
  Often real applications

## Slide 48: Classes of Benchmarks
Toy Benchmarks
  10-100 line–e.g.,: sieve, quicksort
  good first programming assignments
Synthetic Benchmarks
  attempt to match average frequencies of real workloads
  not very useful, too artificial
Kernels
  Time critical excerpts from real programs
    e.g., gcc, spice, Verilog, Databases, stock trading

## Slide 49: SPEC
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
Programs used to measure performance
  Typical of actual workloads

## Slide 50: SPEC CPU 2017
Elapsed time to execute a selection of programs
  Negligible I/O, so focuses on CPU performance
Workload “suites” measure both elapsed time and throughput
  “Speed” integer and “Rate” integer
  “Speed” floating point and “Rate” floating point
Summarizes result as a SPEC ratio

## Slide 51: SPECratios
Normalized relative to reference machine
Geometric mean of performance ratios

## Slide 52: SPEC Benchmarks
SPEC CPU
  CPU performance
SPEC Power
  power consumption
SPEC OMP
  shared memory parallel processing

## Slide 53: Amdahl’s Law
If we could make an improvement to our system to reduce the amount of time it takes to perform a load word instruction by 5%, how much faster would the system run?
  Depends on how often load word is used.

## Slide 54: Amdahl’s Law
The performance enhancement possible with a given improvement is limited by the amount that the improved feature is used.

## Slide 55: Amdahl’s Law
Suppose a program runs in 100 seconds on a computer, with multiply operations responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want my program to run five times faster?
Time affected
Time after improvement = –––––––––– + time unaffected
improvement factor
80
20 Seconds = –––––––––– + (100-80)
improvement factor
80
20 Seconds = –––––––––– + 20
improvement factor
80
0 = ––––––––––
improvement factor

## Slide 56: Amdahl’s Law
Law of diminishing returns
Handy for evaluating impact of a change not tied to CPU performance equation

## Slide 57: Amdahl’s Law: Design Principle
Corollary: make the common case fast
  In many cases the frequency with which one event occurs may be much higher than another.
  Improving the common case will tend to enhance performance better than optimizing the rare case.

## Slide 58: Power Wall
Historically, much of our performance improvements have come from improving our hardware.

## Slide 59: Power Trends

## Slide 60: Reducing Power
The power wall
  We cannot reduce voltage further
Try to remove heat
  Too expensive for common computers
How else can we improve performance?

## Slide 61: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization