## Slide 1: CDA 3103
Recitation 11 – Memory

## Slide 2: Cache Recap
Caches create an illusion of large amounts of fast memory
Cache Details
  Organization: direct mapped, set associative, fully associative
  Write policy: write-through vs. write-back
  Replacement policy: direct, LRU, random

## Slide 3: Cache Example
Assume we have a 2-way set associative cache, with 16 blocks. Each block is one word in width. Show the result (hit/miss) for the following address access sequence and show the final contents of the cache
2, 3, 11, 16, 21, 13, 11, 3, 22, 4, 5, 11

## Slide 4: Cache Example
Address | Tag | Index | Result
2 |  |  | 
3 |  |  | 
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
To find the number of sets divide the total number of blocks by the degree of associativity: 16 / 2

## Slide 5: Cache Example
Address | Tag | Index | Result
2 |  |  | 
3 |  |  | 
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | 
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | 
 | 1 | 
3 | 0 | 
 | 1 | 
4 | 0 | 
 | 1 | 
5 | 0 | 
 | 1 | 
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 
In a 2-way set associative cache each block can be in one of two locations in the set (labeled 0 and 1)

## Slide 6: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 |  |  | 
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | 
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | 
 | 1 | 
4 | 0 | 
 | 1 | 
5 | 0 | 
 | 1 | 
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 7: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 |  |  | 
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | 
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | 
4 | 0 | 
 | 1 | 
5 | 0 | 
 | 1 | 
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 8: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 |  |  | 
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | 
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | 
 | 1 | 
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 9: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 |  |  | 
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | 
 | 1 | 
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 10: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 |  |  | 
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | Mem[21]
 | 1 | 
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 11: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 |  |  | 
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | Mem[21]
 | 1 | Mem[13]
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 12: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 |  |  | 
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | Mem[21]
 | 1 | Mem[13]
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 13: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 |  |  | 
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | Mem[21]
 | 1 | Mem[13]
6 | 0 | 
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 14: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 |  |  | 
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | 
 | 1 | 
5 | 0 | Mem[21]
 | 1 | Mem[13]
6 | 0 | Mem[22]
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 15: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 | 00 | 100 | Miss
5 |  |  | 
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | Mem[4]
 | 1 | 
5 | 0 | Mem[21]
 | 1 | Mem[13]
6 | 0 | Mem[22]
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 16: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 | 00 | 100 | Miss
5 | 00 | 101 | Miss
11 |  |  | 
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | Mem[4]
 | 1 | 
5 | 0 | Mem[5]
 | 1 | Mem[13]
6 | 0 | Mem[22]
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 17: Cache Example
Address | Tag | Index | Result
2 | 00 | 010 | Miss
3 | 00 | 011 | Miss
11 | 01 | 011 | Miss
16 | 10 | 000 | Miss
21 | 10 | 101 | Miss
13 | 01 | 101 | Miss
11 | 01 | 011 | Hit
3 | 00 | 011 | Hit
22 | 10 | 110 | Miss
4 | 00 | 100 | Miss
5 | 00 | 101 | Miss
11 | 01 | 011 | Hit
Set # | Block Position | Contents
0 | 0 | Mem[16]
 | 1 | 
1 | 0 | 
 | 1 | 
2 | 0 | Mem[2]
 | 1 | 
3 | 0 | Mem[3]
 | 1 | Mem[11]
4 | 0 | Mem[4]
 | 1 | 
5 | 0 | Mem[5]
 | 1 | Mem[13]
6 | 0 | Mem[22]
 | 1 | 
7 | 0 | 
 | 1 | 

## Slide 18: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles
Assume a base CPI of 1.

## Slide 19: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.

## Slide 20: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.
With our instruction cache, the effective CPI is (1 + .03*20) = 1.6. The cpu time is IC*CC*1.6

## Slide 21: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.
With our instruction cache, the effective CPI is (1 + .03*20) = 1.6. The cpu time is IC*CC*1.6
Without a cache, the effective CPI is (1+35) = 35. The cpu time is IC*CC*35.

## Slide 22: Cache Performance
Suppose we have a system where the instruction cache has a miss rate of 3% and the miss penalty for the data cache is 20 cycles.
Compare the relative performance of our system to one with an ideal cache and one without caching, where memory access requires 35 cycles.
Assume a base CPI of 1.
With an ideal cache the cpu time is IC*CC.
With our instruction cache, the effective CPI is (1 + .03*20) = 1.6. The cpu time is IC*CC*1.6
Without a cache, the effective CPI is (1+35) = 35. The cpu time is IC*CC*35.
The ideal cache is 1.6 times better than our cache.
Our cache is 21.875 times better than a system without a cache.

## Slide 23: Virtual Memory
The address used by a programmer will be called a logical address
An address in main memory is called a physical address

## Slide 24: Virtual Memory
Only part of the program needs to be in memory for execution
Logical address space can therefore be much larger than physical address space
Allows for more efficient process creation

## Slide 25: Virtual Memory
The term page refers to groups of address space of the same size
For example: if auxiliary memory contains 1024K and main memory contains 32K and page size equals to 1K, then auxiliary memory has 1024 pages and main memory has 32 pages

## Slide 26: Paging
Each process has its own page table
Each page table entry contains the frame number of the corresponding page in main memory
A bit is needed to indicate whether the page is in main memory or not

## Slide 28: Translation Lookaside Buffer
Each virtual memory reference can cause two physical memory accesses
  One to fetch the page table
  One to fetch the data
To overcome this problem a high-speed cache is set up for page table entries
  Called a Translation Lookaside Buffer (TLB)

## Slide 29: Translation Lookaside Buffer
Contains page table entries that have been most recently used
Given a virtual address, processor examines the TLB
If page table entry is present (TLB hit), the frame number is retrieved and the real address is formed
If page table entry is not found in the TLB (TLB miss), the page number is used to index the process page table

## Slide 30: Translation Lookaside Buffer
First checks if page is already in main memory
  If not in main memory a page fault is issued
The TLB is updated to include the new page entry

## Slide 35: Questions?