## Slide 1: Memory
Memory Hierarchy: Caches

## Slide 2: Introduction
An ideal computing system has unlimited fast memory
  Obviously, this is not possible
  A memory hierarchy gives the illusion of large amounts of fast memory

## Slide 3: Principle of Locality
Programs access only a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 4: Memory Hierarchy
Smaller, faster memory is closer to the processor

## Slide 5: Caches
Permanent storage on disk
Copy recently accessed and nearby items from disk to smaller DRAM memory
  Main memory
Copy recently accessed and nearby items from DRAM to smaller SRAM memory
  Cache memory attached to CPU
  Cache may also refer to any storage that takes advantage of locality

## Slide 6: Memory Hierarchy Levels
Block: unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 7: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
How do we know if the data is present?
Where do we look?

## Slide 8: Direct Mapped Cache
Each word can go in exactly one place in the cache
  Assign a location based on the address of the word
  (Block address) modulo (#Blocks in cache)

## Slide 9: Direct Mapped Cache
Each word can go in exactly one place in the cache
  Assign a location based on the address of the word
  (Block address) modulo (#Blocks in cache)

## Slide 10: Direct Mapped Cache
Each word can go in exactly one place in the cache
  Assign a location based on the address of the word
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 11: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 12: Cache Read
Reads are simpler because reads do not change the contents of the cache
Example:
  8-Block, Direct Mapped Cache
  Addresses:
  Binary Decimal Cache Block (address mod 8)
  10110 22 110
  11010 26 010
  10110 22 110
  11010 26 010
  10000 16 000
  00011 3 011
  10000 16 000
  10010 18 010
  10000 16 000

## Slide 13: Cache Example
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 14: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 15: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 16: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 17: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 18: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 19: Address Subdivision

## Slide 20: Cache Hit
Index of the address specifies cache block
If the valid bit indicates data is present, check the tags
If the tags match, it is a hit
We can use the data stored in the cache
CPU proceeds normally

## Slide 21: Cache Misses
If the valid bit is not set or if the tags do not match, it is a miss
Control unit must detect and process a miss
  Creates a stall in the pipeline

## Slide 22: Cache Miss (Instruction Memory)
Send the original PC value (current PC – 4) to the memory.
Instruct main memory to perform a read and wait for the memory to complete its access.
Write the cache entry, putting the data from memory in the data portion of the entry, writing the upper bits of the address (from the ALU) into the tag field, and turning the valid bit on.
Restart the instruction execution at the first step, which will refetch the instruction, this time finding it in the cache.

## Slide 23: Cache Miss
Stall until the data is fetched from memory
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 24: Cache Miss
Misses are classified into three different types
Compulsory (cold start)
  First access to a piece of data
  Cannot be avoided
Capacity
  Working set of program is larger than cache size
  Not enough room to cache a locality
Conflict
  collisions, multiple blocks competing for the same space
Misses may be reduced by changing the associativity of the cache

## Slide 25: Cache Organizations
Direct mapped
Set associative
Fully associative

## Slide 26: Fully Associative
A block in memory may be associated with any entry in the cache
Requires all entries to be searched at once
Comparator per entry (expensive)

## Slide 27: N-way Set Associative
Each block may go to n locations
Each set contains n entries
Block number determines which set
  (Block number) modulo (#Sets in cache)
Search all entries in a given set at once
n comparators (less expensive)

## Slide 28: Associative Cache Example

## Slide 29: Associativity
All cache organizations are a variation of set associativity.
Direct mapped: 1-way set associative
Fully associative: m-way associative where m is the number of blocks in the cache

## Slide 30: Spectrum of Associativity
For a cache with 8 entries

## Slide 31: Set Associative Cache Organization

## Slide 32: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 33: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3

## Slide 34: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 

## Slide 35: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 

## Slide 36: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 

## Slide 37: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 

## Slide 38: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 39: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
5 misses
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 40: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 

## Slide 41: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 

## Slide 42: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 

## Slide 43: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 

## Slide 44: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 

## Slide 45: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 

## Slide 46: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
4 misses
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 

## Slide 47: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Fully associative
3 misses
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 48: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB cache, 16-word blocks
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 49: Cache Write
If we replace the data memory in our datapath with a cache, what happens on a store word instruction?
If we wrote the data into only the data cache without changing main memory; then main memory would have a different value from that in the cache.
  In such a case, the cache and memory are said to be inconsistent.

## Slide 50: Write-Through
Whenever changes are made to the data in the cache, also change the data in main memory.

## Slide 51: Write-Through
Whenever changes are made to the data in the cache, also change the data in main memory.
Writes take longer
  Suppose 10% of instructions are stores and write to memory takes 100 cycles
  If base CPI = 1, then effective CPI = 1 + 0.1×100 = 11

## Slide 52: Write-Through
Whenever changes are made to the data in the cache, also change the data in main memory.
Writes take longer
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 53: Write-Back
On data-write hit, just update the block in cache
  Keep track of whether each block is “clean” or “dirty”
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 54: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 55: Performance
The time to service hits and misses affects the CPU time.
  Hit time
    time required to access the cache
    includes time to determine if it’s a hit or a miss
  Miss penalty
    time required to fetch a block from the next lowest level
  Hit time < Miss penalty

## Slide 56: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
CPU time = (CPU cycles + Memory-stall cycles) * Clock cycle time
Memory-stall cycles = Read-stall cycles + Write-stall cycles
Read-stall cycles = Reads/Program * Read miss rate * Read miss penalty
Write-stall cycles = (Writes/Program * write miss rate * write miss penalty) + Write buffer stalls

## Slide 57: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses

## Slide 58: Cache Performance Example
Assume an instruction cache miss rate for a program is 2% and a data cache miss rate is 4%. If a processor has a CPI of 2 without any memory stalls and the miss penalty is 100 cycles for all misses, determine how much faster a processor would run with a perfect cache that never missed. Assume the frequency of all loads and stores is 36%.

## Slide 59: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions

## Slide 60: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions
Determine miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
  Memory miss cycles = 2 + 1.44 = 3.44

## Slide 61: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions
Determine miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
  Memory miss cycles = 2 + 1.44 = 3.44
Actual CPI = 2 + 3.44 = 5.44

## Slide 62: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Base CPI (ideal cache) = 2
  Miss penalty = 100 cycles
  Load & stores are 36% of instructions
Determine miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
  Memory miss cycles = 2 + 1.44 = 3.44
Actual CPI = 2 + 3.44 = 5.44
Ideal CPU is 5.44/2 =2.72 times faster

## Slide 63: Performance Considerations
What happens if the processor is made faster, but the memory system is not?
  The amount of time spent on memory stalls will take up an increasing fraction of the execution time
  Amdahl’s law

## Slide 64: Cache Performance Example Revisit
Suppose we speed up the system by reducing its CPI from 2 to 1 without changing the clock rate.
  Actual CPI = 1 + 3.44 = 4.44
  Ideal CPU is 4.44/1 = 4.44 times faster
Amount of time spent on memory stalls increases:
  Before: 3.44/5.44 = 63%
  Now: 3.44/4.44 = 77%

## Slide 65: Performance Considerations
Increasing clock rate without changing the memory system also increases the performance lost due to cache misses.
  Memory stalls account for more CPU cycles

## Slide 66: Performance Considerations
Hit Access Time
  If the hit time increases, the total time to access a word from the memory system will increase.
  Affect by:
    Cache size
    Number of pipeline stages
    Cache organization

## Slide 67: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 68: Multilevel Cache Example
Suppose we have a processor with a base CPI of 1.0, assuming all references hit in the primary cache, and a clock rate of 5 GHz. Assume a main memory access time of 100 ns, including all the miss handling. Suppose the miss rate per instruction at the primary cache is 2%.
How much faster will the processor be if we add a secondary cache that has a 5 ns access time for either a hit or a miss and is large enough to reduce the miss rate to main memory to 0.5%?

## Slide 69: Multilevel Cache Example
Given
  CPU base CPI = 1
  CPU clock rate = 5 GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns

## Slide 70: Multilevel Cache Example
Given
  CPU base CPI = 1
  CPU clock rate = 5 GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.2ns = 500 cycles
  Effective CPI = 1 + 0.02 × 500 = 11

## Slide 71: Multilevel Cache Example
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.2ns = 25 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 25 + 0.005 × 500 =4
Performance ratio = 11/4 = 2.8

## Slide 72: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 73: Summary
Cost/Performance tradeoff in memory technologies
  Create an illusion of large amounts of fast memory with a hierarchy
  Uses caches close to the processor
Cache Details
  Organization: direct mapped, set associative, fully associative
  Write policy: write-through vs. write-back
  Replacement policy: direct, LRU, random

## Slide 74: Summary
Tradeoffs to Improve Cache Performance:
  Use better technology
    Use faster RAMs
    Cost and availability are limitations
  Decrease Hit Time
    Make cache smaller, but miss rate increases
    Use direct mapped, but miss rate increases
  Decrease Miss Rate
    Make cache larger, but can increases hit time
    Add associativity, but can increase hit time
    Increase block size, but increases miss penalty
  Decrease Miss Penalty
    Reduce transfer time component of miss penalty
    Add another level of cache