## Slide 1: CDA 3103
Recitation 3 – Karnaugh Maps

## Slide 2: Logic Minimization
Our goal is to create a minimal representation of logic functions
This is done by:
  Rewrite the function as the sum of its minterms
    Sum of products canonical form
  Place minterms in a Karnaugh map
  Use Karnaugh map to determine the minimal function

## Slide 3: Review: Minterms
A minterm is a special product of literals, in which each input variable appears exactly once.
A function with n variables has 2n minterms (since each variable can appear complemented or not)
A three-variable function, such as f(x,y,z), has 23 = 8 minterms:
Minterm Is true when… Shorthand
x’y’z’ x=0, y=0, z=0 m0
x’y’z x=0, y=0, z=1 m1
x’yz’ x=0, y=1, z=0 m2
x’yz x=0, y=1, z=1 m3
xy’z’ x=1, y=0, z=0 m4
xy’z x=1, y=0, z=1 m5
xyz’ x=1, y=1, z=0 m6
xyz x=1, y=1, z=1 m7

## Slide 4: Review: Karnaugh Maps
A two-variable function has four possible minterms. We can re-arrange these minterms into a Karnaugh map.

## Slide 5: Review: Karnaugh Maps
Now we can easily see which minterms contain common literals.
  Minterms on the left and right sides contain x’ and x respectively.
  Minterms in the top and bottom rows y’ and y respectively.

## Slide 6: Review: Karnaugh Maps
Imagine a two-variable sum of minterms:
x’y’ + x’y
Both of these minterms appear in the left column of a Karnaugh map, which means that they both contain the literal x’.
What happens if you simplify this expression using Boolean algebra?
x’y’ + x’y = x’(y’ + y) [ Distributive ]
= x’  1 [ y + y’ = 1 ]
= x’ [ x  1 = x ]

## Slide 7: Review: Karnaugh Maps
For a three-variable expression with inputs x, y, z, the arrangement of minterms is more tricky:
Another way to label the K-map

## Slide 8: Review: Karnaugh Maps
With this ordering, any group of 2, 4 or 8 adjacent squares on the map contains common literals that can be factored out.
“Adjacency” includes wrapping around the left and right sides:
x’y’z + x’yz
= x’z(y’ + y)
= x’z  1
= x’z
Notes: Discuss gray code here

## Slide 9: Review: Karnaugh Maps
We’ll use this property of adjacent squares to do our simplifications.
x’y’z + x’yz
= x’z(y’ + y)
= x’z  1
= x’z
  x’y’z’ + xy’z’ + x’y’z + xy’z
  = y’(x’z’ + xz’ + x’z + xz)
  = y’(z’(x’ + x) + z(x’ + x))
  = y’(z’+z)
  = y’
Notes: Discuss gray code here.  The problem with natural binary codes is that, with real (mechanical) switches, it is very unlikely that switches will change states exactly in synchrony. In the transition between the two states shown 011  100, all three switches change state. In the brief period while all are changing, the switches will read some spurious position. Even without keybounce, the transition might look like 011 — 001 — 101 — 100. When the switches appear to be in position 001, the observer cannot tell if that is the "real" position 001, or a transitional state between two other positions. If the output feeds into a sequential system (possibly via combinational logic) then the sequential system may store a false value.
The reflected binary code solves this problem by changing only one switch at a time, so there is never any ambiguity of position,
Dec Gray Binary
0 000 000
1 001 001
2 011 010
3 010 011
4 110 100
5 111 101
6 101 110
7 100 111
Notice that state 7 can roll over to state 0 with only one switch change. This is called the "cyclic" property of a Gray code.
In gray code only one bit position changes between any two successive (nearby) entries. This allows us to group the terms producing the same output(normally 1) and eliminate the variable corresponding to the common bit position. As the K-map is used for reduction of min terms, this approach is used. It is the basis of the K-map itself.
In a Karnaugh map the boolean variables are transferred (generally from a truth table) and ordered according to the principles of Gray code in which only one variable changes in between squares. Once the table is generated and the output possibilities are transcribed, the data is arranged into the largest even group possible and the minterm is generated through the axiom laws of boolean algebra!!

## Slide 10: Example K-map simplification
Let’s consider simplifying f(x,y,z) = xy + y’z + xz.
First, you should convert the expression into a sum of minterms form, if it’s not already.
  The easiest way to do this is to make a truth table for the function, and then read off the minterms.
  You can either write out the literals or use the minterm shorthand.

## Slide 11: Example K-map simplification
Let’s consider simplifying f(x,y,z) = xy + y’z + xz.
  Here is the truth table and sum of minterms for our example:
f(x,y,z) = x’y’z + xy’z + xyz’ + xyz
= m1 + m5 + m6 + m7

## Slide 12: Unsimplifying expressions
You can also convert the expression to a sum of minterms with Boolean algebra.
  Apply the distributive law in reverse to add in missing variables.
  Very few people actually do this, but it’s occasionally useful.
In both cases, we’re actually “unsimplifying” our example expression.
  The resulting expression is larger than the original one!
  But having all the individual minterms makes it easy to combine them together with the K-map.
xy + y’z + xz = (xy  1) + (y’z  1) + (xz  1)
= (xy  (z’ + z)) + (y’z  (x’ + x)) + (xz  (y’ + y))
= (xyz’ + xyz) + (x’y’z + xy’z) + (xy’z + xyz)
= xyz’ + xyz + x’y’z + xy’z

## Slide 13: Making the example K-map
Next up is drawing and filling in the K-map.
  Put 1s in the map for each minterm, and 0s in the other squares.
  You can use either the minterm products or the shorthand to show you where the 1s and 0s belong.
In our example, we can write f(x,y,z) in two equivalent ways.
In either case, the resulting K-map is shown below.
f(x,y,z) = x’y’z + xy’z + xyz’ + xyz
f(x,y,z) = m1 + m5 + m6 + m7

## Slide 14: K-maps from truth tables
You can also fill in the K-map directly from a truth table.
  The output in row i of the table goes into square mi of the K-map.
  Remember that the rightmost columns of the K-map are “switched.”
f(x,y,z) = m1 + m5 + m6 + m7

## Slide 15: Grouping the minterms together
The most difficult step is grouping together all the 1s in the K-map.
  Make rectangles around groups of one, two, four or eight 1s.
  All of the 1s in the map should be included in at least one rectangle.
  Do not include any of the 0s.

## Slide 16: Grouping the minterms together
Each group corresponds to one product term. For the simplest result:
  Make as few rectangles as possible, to minimize the number of products in the final expression.
  Make each rectangle as large as possible, to minimize the number of literals in each term.
  It’s all right for rectangles to overlap, if that makes them larger.

## Slide 17: Reading the MSP from the K-map
Finally, you can find the minimal sum of products (MSP).
  Each rectangle corresponds to one product term.
  The product is determined by finding the common literals in that rectangle.
For our example, we find that xy + y’z + xz = y’z + xy.

## Slide 18: Practice K-map 1
Simplify the sum of minterms, f(x,y,z) = m1 + m3 + m5 + m6.

## Slide 19: Solutions for practice K-map 1
Here is the filled in K-map, with all groups shown.
  The blue and green groups overlap, which makes each of them as large as possible.
  Minterm m6 is in a group all by its lonesome.
The final MSP here is x’z + y’z + xyz’.

## Slide 20: Four-variable K-maps
We can do four-variable expressions too!
  The minterms in the third and fourth columns, and in the third and fourth rows, are switched around.
  Again, this ensures that adjacent squares have common literals.
Grouping minterms is similar to the three-variable case, but:
  You can have rectangular groups of 1, 2, 4, 8 or 16 minterms.
  You can wrap around all four sides.

## Slide 21: Simplify f(w, x, y, z) = m0+m2+m5+m8+m10+m13
The expression is already a sum of minterms, so here’s the K-map:

## Slide 22: Simplify f(w, x, y, z) = m0+m2+m5+m8+m10+m13
We can make the following groups, resulting in the MSP x’z’ + xy’z.

## Slide 23: K-maps can be tricky!
There may not necessarily be a unique MSP. The K-map below yields two valid and equivalent MSPs, because there are two possible ways to include minterm m7.
Remember that overlapping groups is possible, as shown above.
x’y + xy’ + xz
x’y + xy’ + yz

## Slide 24: Prime implicants
The challenge in using K-maps is selecting the right groups. If you don’t minimize the number of groups and maximize the size of each group:
  Your resulting expression will still be equivalent to the original one.
  But it won’t be a minimal sum of products.
Notes: 24

## Slide 25: Prime implicants
First find all of the largest possible groupings of 1s.
  These are called the prime implicants.
  The final MSP will contain a subset of these prime implicants.
Here is an example Karnaugh map with prime implicants marked:
Notes: 25

## Slide 26: Essential prime implicants
If any group contains a minterm that is not also covered by another overlapping group, then that is an essential prime implicant.
Essential prime implicants must appear in the MSP, since they contain minterms that no other terms include.
Our example has just two essential prime implicants:
  The red group (w’y’) is essential, because of m0, m1 and m4.
  The green group (wx’y) is essential, because of m10.
Notes: 26

## Slide 27: Covering the other minterms
Finally pick as few other prime implicants as necessary to ensure that all the minterms are covered.
After choosing the red and green rectangles in our example, there are just two minterms left to be covered, m13 and m15.
  These are both included in the blue prime implicant, wxz.
  The resulting MSP is w’y’ + wxz + wx’y.
The black and yellow groups are not needed, since all the minterms are covered by the other three groups.
Notes: 27

## Slide 28: Practice K-map 2
Simplify for the following K-map:
Notes: 28

## Slide 29: Solutions for practice K-map 2
Simplify for the following K-map:
All prime implicants are circled.
Essential prime implicants are x’z, yz and wx.
The MSP is x’z + yz + wx.
(Including the group wz would be redundant.)
Notes: 29

## Slide 30: Practice K-map 3
Find a MSP for
f(w,x,y,z) = m(0,2,4,5,8,14,15) + d(7,10,13)
This notation means that input combinations wxyz = 0111, 1010 and 1101 (corresponding to minterms m7, m10 and m13) are unused or don’t cares.
Notes: 30

## Slide 31: Solutions for practice K-map 3
All prime implicants are circled. We can treat X’s as 1s if we want, so the red group includes two X’s, and the light blue group includes one X.
The only essential prime implicant is x’z. The red group is not essential because the minterms (1’s) in it also appear in other groups.
The MSP is x’z’ + wxy + w’xy’. It turns out the red group is redundant; we can cover all of the minterms in the map without it.
f(w,x,y,z) = m(0,2,4,5,8,14,15) + d(7,10,13)
Notes: 31