## Slide 1: Midterm Review
Binary Conversions, Combinational Logic Design, Arithmetic Hardware, Binary Arithmetic, MIPS Assembly

## Slide 2: Notes
Available on webcourses from Thursday, March 11th through Saturday, March 13th
11 questions
75 minutes
Respondus LockDown Browser Required
  Will still allow access to webcourses for notes
  Will provide on screen calculator, but you can also use your own
  No webcam required
Open book / Open notes
  Just not “open internet” or “open friend”

## Slide 3: Introduction to Binary
Binary Conversions
  Unsigned
  2’s Complement

## Slide 4: Sample Question
Consider the binary number A = 1101. What is the decimal representation of A, if A is expressed as an:
  Unsigned number
  2’s complement number

## Slide 5: Arithmetic Hardware
Ripple-Carry Adder
Arithmetic Logic Unit
  Inputs
  Outputs
  Functions

## Slide 6: Sample Question
If A = 1101 and B = 0011, and both are 2’s complement numbers, determine A-B. State if overflow occurs.

## Slide 7: Combinational Logic Design
Truth Tables
Logic Gates
Canonical Forms
Karnaugh Maps

## Slide 8: Sample Question
Implement a combinational logic system that has two data inputs (A and B), one select input S, and one data output F. If S=0, then F=A, and if S=1, then F=B.

## Slide 9: Computer Arithmetic
Multiply and Divide Integers
  Booth’s Algorithm
Floating Point representation
  IEEE 754

## Slide 10: Sample Question
Multiply the following two signed numbers using Booth’s algorithm:
10100110 x 01110110

## Slide 11: Sample Question
Convert 220.2 (base 10) to IEEE-754 single precision floating point format.

## Slide 12: MIPS ISA
Assembly Operations
  Arithmetic (add, addi)
  Logical (and, or, andi, ori, slt, slti)
  Load/Store (lw, sw)
  Branches (beq, j)
Instruction Formats
  R-Type
  I-Type
  J-Type

## Slide 13: Sample Question
What value is contained in $t2 upon completion of the MIPS code below:
addi $t1, $zero, 1
sll $t2, $t1, 8

## Slide 14: Sample Question
Consider the following segment of C code where the variables {u, w, z} reside in {$t1,$t2,$t3} respectively. Complete the corresponding assembly language fragment by writing in the correct instruction or register
while (u == w) { while: __________ $t1, $t2, exit
u = u + 1; __________ $t1, $t1, 1 w = u – z; sub _______, _______, _______
} __________ while
exit: