## Slide 1: CDA 3103
Project Details

## Slide 2: Project overview
Simulate a MIPS processor in C
  There a three files: spimcore.c, spimcore.h, and project.c
  Your task is to fill in the functions in project.c
  These functions are called by the “step” function in spincore.c
  spimcore.h contains the prototypes for the functions and the control signal structure definition

## Slide 3: Misconceptions
You should not make any changes to spimcore.c or spimcore.h
You do not require any input/output functions
  these are handled by spimcore.c
You do not need to convert between HEX and/or DEC

## Slide 4: Development Environment Options
MUST compile with gcc
Linux (Virtual Machine or otherwise)
  $ gcc -o spimcore spimcore.c project.c
  $ ./spimcore <filename>.asc

## Slide 5: Controls
R | Show register contents
M | Show memory contents
S | Step forward 1 instruction
C | Continue all instructions until halt
H | Check to see if program has halted
X | Quit

## Slide 6: IF
int instruction_fetch(unsigned PC, unsigned *Mem, unsigned *instruction)
Mem is an array and has already been populated
PC is the current index to use for instruction memory
Check for word alignment
Use PC >> 2 to get the actual location (because Mem is an array of words in C, instead of an array of bytes)

## Slide 7: IP
void instruction_partition(unsigned instruction, unsigned *op, unsigned *r1,unsigned *r2, unsigned *r3, unsigned *funct, unsigned *offset, unsigned *jsec)
unsigned op, // instruction [31-26]
r1, // instruction [25-21]
r2, // instruction [20-16]
r3, // instruction [15-11]
funct, // instruction [5-0]
offset, // instruction [15-0]
jsec; // instruction [25-0]
No need to check the opcode here, make copies of all sections regardless of instruction type.

## Slide 8: ID
int instruction_decode(unsigned op,struct_controls *controls)
typedef struct {
char RegDst;
char Jump;
char Branch;
char MemRead;
char MemtoReg;
char ALUOp;
char MemWrite;
char ALUSrc;
char RegWrite;
} struct_controls;
Based on the opcode, set the control signals in the controls structure. These are stored in the character data type, but do not have to be characters (the data type just provides a “box” that is 8 bits wide). Most signals are either 0 or 1. ALUOp is a 3 bit signal in this project.

## Slide 9: Read register
void read_register(unsigned r1,unsigned r2,unsigned *Reg,unsigned *data1,unsigned *data2)
Reg is an array containing the register file

## Slide 10: Sign Extend
void sign_extend(unsigned offset,unsigned *extended_value)
16th bit is the sign bit
During instruction_partition, you may have put all zeros in the upper order 16 bits. In that case, you would only need to change the value if the sign bit is negative.

## Slide 11: ALU_operations
int ALU_operations(unsigned data1,unsigned data2,unsigned extended_value,unsigned funct,char ALUOp,char ALUSrc,unsigned *ALUresult,char *Zero)
Set parameters for A, B, and ALUControl
If R-type instruction, look at funct
In the end, call ALU function

## Slide 12: rw_memory
int rw_memory(unsigned ALUresult,unsigned data2,char MemWrite,char MemRead,unsigned *memdata,unsigned *Mem)
Mem is the memory array
If MemWrite = 1, check word alignment and write into memory
If MemRead = 1, check word alignment and read from memory

## Slide 13: write_register
void write_register(unsigned r2,unsigned r3,unsigned memdata,unsigned ALUresult,char RegWrite,char RegDst,char MemtoReg,unsigned *Reg)
If RegWrite == 1, and MemtoReg == 1, then data is coming from memory
If RegWrite == 1, and MemtoReg == 0, then data is coming from ALU_result
If RegWrite == 1, place write data into the register specified by RegDst

## Slide 14: PC_update
void PC_update(unsigned jsec,unsigned extended_value,char Branch,char Jump,char Zero,unsigned *PC)
PC = PC + 4;
Take care of Branch and Jump
Zero – Branch taken or not
Jump: Left shift bits of jsec by 2 and use upper 4 bits of PC

## Slide 15: Hints
Accessing memory
  Mem[0] is an unsigned int, aka the whole WORD.
  This means that given an address, like the PC, you need to shift the address to the RIGHT by 2 to form the index for the Mem structure.
Notes: so you would say Mem[PC>>2] to get the word pointed to by the PC.
Use the macro!
    This gets annoying which is why there is already a macro provided called MEM. So you can say things like unsigned int instruction = MEM(PC); and the MEM macro takes the arg (PC) and shifts it right by 2 for you. It’ll save your sanity later.

## Slide 16: Hints
Isolating bits in an unsigned int can be done with a bitwise AND and shift in C. For example:
  int op = (inst & 0xFC000000) >> 26;
  int op = (inst & 0b11111100000000000000000000000000) >> 26;
The input is a series of HEX numbers representing instructions.
  Don’t write anything to parse this file, this is handled by spimcore.c.
  Those numbers are already sitting in the Mem array at the proper address.
  They do not need to be converted in order to do operations like AND and shift as shown above.
Notes: so you would say Mem[PC>>2] to get the word pointed to by the PC.
Make a macro!
    This gets annoying which is why there is already a macro provided called MEM. So you can say things like unsigned int instruction = MEM(PC); and the MEM macro takes the arg (PC) and shifts it right by 2 for you. I typically encourage everyone to use the macro after explaining this. This will save them later.

## Slide 17: Questions?